Script descriptions reference document:
- all scripts are shell scripts meant to speedup experiment procedures
- many scripts use sshpass system to send over commands over ssh to rpi’s
- in the event that the static IP of any rpi changes or the rpi needs to change update the static IP of called as well as the password.

Run a script:
- open file directory to /Documents/Scripts
- run script using the command “ ./name_of_script.sh”
Create a new script:
- open file directory to /Documents/Scripts
- create a text file called “name_of_script.sh”
- add the following line at the start of the script ”#!/bin/bash “
- save the script and then run the command “chmod +x name_of_script.sh”

IP address reference:

System initialize: scripts meant to startup systems

init_threat_filed.sh:
- overall system initialize, runs other initialize scripts
- use to run entire experiment

init_cam_sys.sh:
- sends command turtlebot mounted rpi (not internal, but the one with the cameras attached) to initialize sending over camera readings
- currently the IP is root@192.168.1.16 with password “letmein” (change if needed)
- after running you should see camera readings in the “ColorVals” ROS message

init|_dynamicfield.sh:
- runs threat field generator python code that outputs the threat field as an image file,
- the python code can be edited to either run a static field based on Gaussian algorithm or a dynamic field based on solutions to the advection diffusion equations
init_nav.sh:
- initiates the turtlebots navigation algorithm
- ssh into Turtlerbot (internal) computer with IP: root@192.168.1.15 with password “letmein” (change if needed)

init_projectors.sh:
initiate the projectors by ssh into all four and running the projector.py python code that uses sxiv program to display the images in the folder.

System Shutdown:

stop_threat_field.sh: over all system shutdown
stop_projectors.sh: ssh into projectors and stops image viewing
proj_shutdown.sh: ssh into projectors and shuts them down
stop_nav.sh: ssh into turtlebot and stop navigation
stop_cam.sh: ssh into cam rpi and stop camera output

Other Systems:

umount_all.sh: if using nfs for file transfer this umounts all nfs from rpis of projectors
remount_all.sh: if using nfs for file transfer this umount and remounts all rpi of projectors.
Restart.sh: restarts projector rpis